## Slide 1: IPv6
Geoff Huston
APNIC

## Slide 2: Why?

## Slide 3: Because we ran out of IP addresses

## Slide 4: Again.

## Slide 5: We’ve been here before ...
The original ARPAnet design from 1969 used the NCP protocol, which used 8 bit addresses in the NCP packet header
  Maximum network span of 256 nodes
  Enough?
  Well yes, because at the time computers were the size of entire rooms, cost many millions of dollars and there were only a few thousand in the entire world.
  At the time the entire concept of shrinking the computer to something you could hold in one hand and trying to connect billions of them together was just too far into the future to worry about

## Slide 6: Transition V1.0
Turns out that 8 bits of addresses was not enough for the next generation of mini-computers
ARPAnet undertook a transition from NCP to a new protocol: TCP/IP
  Expansion from 8-bit to 32-bit addresses
  Flag Day: 1 January 1983
  Shutdown and reboot every node into the new protocol!

## Slide 7: “This time, for sure!” *
* Actually Vint didn’t say this!

## Slide 8: IP Version 4
32-bit address field
  That’s 4,294,967,296 addresses
In 1983 that looked like a HUGE number of computers

## Slide 9: Digital Pressures
Through the 1980’s computers changed from large expensive pieces of ironware to desktop consumer products
  And the market changed from thousands to tens of millions
And the prospect was smaller, cheaper and more
  So by 1990 that 4 billion address space was looking pretty small
  And it was not going to last much longer!
Frank Solensky – IETF 1990
Presentation on IPv4 Address Depletion Predictions

## Slide 10: IPocalypse?

## Slide 11: So we hit the wall – right?

## Slide 12: Panic!
This was a brutal wakeup call
We had hardly started with the internet and its demise was just 4 years away!
So we rapidly worked on short term responses to push this exhaustion date out
To give us more time to work on the longer term solutions
So:
  We dropped the classful address plan
  We introduced NATs to allow address sharing
  We worked on a new protocol

## Slide 13: It worked!
NSFNET
A&R networks
CIDR
Boom & Bust
GFC
Exhaustion!
Broadband
Mobiles
The short term response to imminent depletion

## Slide 14: That longer term plan
Was to develop a new IP protocol
And then transition the Internet over to use this new protocol

## Slide 15: What are we transitioning to?

## Slide 16: IPv6!

## Slide 17: IPv6 is…
IPv4 with larger address fields
Not much else changed
  It’s still an address-based stateless datagram forwarding protocol
  It still has decoupled forwarding, routing, naming, transport
  The interfaces to the underlying media protocols are largely unchanged
So transition to IPv6 should be easy

## Slide 18: So transition should be easy?
Right?

## Slide 19: So transition should be easy?
Well, no, not really!

## Slide 20: Why is this taking so long?
IPv6 was a minimal change to IPv4
  So early adopters found little in the way of an early adoption benefit
IPv6 was not backward compatible with IPv4
  IPv6 adopters still had to support IPv4
  EVERYONE has to transition to dual stack BEFORE we can drop IPv4

## Slide 21: Transition, the second time around
A “Flag Day” switchover is impossible
Piecemeal replacement won’t work either, as IPv6 is not backward compatible with IPv4
So, we need to run both protocols in tandem “for a while”
But bear in mind that one protocol has already run out of addresses
And network growth continues at record levels

## Slide 22: Transition, the second time around
We need to :
deploy IPv6 in parallel with IPv4
deploy ever more stringent IPv4 address conservation measures within the network
allow the network to expand at an ever-increasing rate
All at the same time!

## Slide 23: Transition is more like this!

## Slide 24: Or this!

## Slide 25: “The Internet” does not exist
The Internet is not a singly managed entity
Noone is in control
Noone is there to tell anyone else what they can (or cannot) do
The Internet is a collection of markets (Goods and services, Transmission and switching, Technologies, …)
We find it impossible to orchestrate collective synchronised actions across all these distinct activities
So the status quo accumulates a huge amount of inertial momentum
Which makes it terribly hard to change direction in an orderly manner!

## Slide 26: Its now 2022 and we are still in this transition
We underestimated the awesome ability of NATs to squeeze out address efficiencies – the past decade of massive growth on the Internet has been largely based on various forms of NAT usage
NATs expanded the usable IPv4 address capacity by a further ~20 bits
  Each bit of increased address size doubles the total capacity of the space
  So it’s taken us much longer than we though to fill up these additional address bits

## Slide 27: So how is this transition going?
Slowly!

## Slide 28: Let’s look at progress so far
2012 – no significant deployment of IPv6

## Slide 29: Let’s look at progress so far
2012
2014 – still very little movement in the larger environment

## Slide 30: Let’s look at progress so far
2012
2014
2017 – India IPv6 deployment

## Slide 31: Let’s look at progress so far
2012
2014
2017
2019 – stirring in China

## Slide 32: Where are we in 2022?
11 years after the depletion of the central IPv4 address pools we are still sitting on some 30% of the Internet user base with Dual Stack (IPv4 + IPv6) support
  The other 3 billion uses are on IPv4 only
How much longer will it take before we can call this transition “completed”?

## Slide 33: Why is this taking so long?
If we designed the IPv6 protocol 30 years ago
And we’ve been running the IPv4 Internet on empty for many years
Then why isn’t the Internet an all-IPv6 Internet today?

## Slide 34: Why is this taking so long?
NATs are just too good!
  NATs drive every part of today’s internet, and we’ve adapted the entire IP infrastructure and application space to work in a NAT environment
  We’ve pushed the role of service identification to the name space
  And changed the architecture of the Internet into a client/server model
  And clients don’t need permanently assigned public addresses
  So NATs have allowed us to build a network with some 40 billion connected devices – and we are confident that we can grow further

## Slide 35: Why is this taking so long?
IPv6 is not different enough
  IPv6 is just IPv4 with larger addresses
  It does not make packet switching any cheaper, so it does not give early adopters any advantage
  And IPv6 not backward compatible with IPv4, so early adopters still have to run IPv4 as well

## Slide 36: Why is this taking so long
The transition timetable is not being set by the early adopters
  There is not enough competitive advantage for early adopters to drive the transition
The transition timetable is not being set by the late adopters
  At some point the last to adopt cannot impose a hold over everyone else
So transition is a form of “majority” decision making
  It’s a case of “critical mass” that will determine at what point dual stack service providers will contemplate dropping IPv4 and completing their part of the transition

## Slide 37: IPv6 Adoption today
0
Not everywhere – not all at once
~1 B IPv6 users out of 4B

## Slide 38: Asia
900M IPv6 users out of 2.3 B

## Slide 39: India

## Slide 40: China

## Slide 41: Malaysia

## Slide 42: Singapore
What’s this?
It’s likely to be the combination of Cloudflare and Apple’s recent Private Relay service
https://www.theregister.com/2022/05/11/internet_has_shrunk/

## Slide 43: Market Signals
The Price of IPv4 Addresses

## Slide 44: Conclusions
Is this transition was coming to an end the price of IPv4 addresses on the market would be collapsing
  Instead it doubled over 2021!
  So it seems that this transition will continue for some time yet
There is no Plan B
  There is no alternative to IPv6 out there, and continued growth of the silicon base continues to drain IPv4 resources
  The escalating IPv4 price makes staying in IPv4-only less and less tenable
So its not a case of “if” IPv6, but a case of “when” IPv6

## Slide 45
Thanks!